## Slide 1: Swift: Delay is Simple and Effective for Congestion Control in the Datacenter
Raghuveer Sharma Saripalli (50946752)
Yamini Palnati (98601457)
Tejasri Dontham (81715873)

## Slide 2: Motivation and Problem Definition

## Slide 3: What is Congestion Control?
Congestion control is a way to modulate traffic entering a network in order to avoid congestion collapse.
This is typically accomplished by reducing the rate of packets sent from sender to receiver and traditionally we also differentiate the congestion control that prevents sender from overwhelming the network and also another thing is the flow control that prevents sender from overwhelming the receiver.

## Slide 4: Motivation
New latency-sensitive applications/ media heterogeneity.
Large-scale incast for partition aggregate workflows.
IOPS intensive applications, like BigQuery Shuffle operation
Increased line rate – 100 Gbps and beyond.

## Slide 5
With the increasing demand for high bandwidth, we should be able to provide a near-zero loss and high throughput.
We need an end-to-end congestion control that manages congestions in hardware and software.

## Slide 6: SOLUTION

## Slide 7: Main Idea
Swift is based on delay.
Accurate RTT measurements
Treat host and fabric delays separately.
Pacing packet is not CPU efficient compared to ACK clocking.

## Slide 8: Decoupled host and fabric delays
Click to add text
Click to add text

## Slide 9
End point delay:
(t4-t2)+t6-t5
Fabric delay:
(t6-t1)-endpoint delay
Decoupled host and fabric delays

## Slide 10: Additive increment multiplicative decrease
Swift allows cwnd to fall below 1 to handle large-scale incast.

## Slide 11: Additive increment multiplicative decrease
Click to add text

## Slide 12: Fabric and host delays
Host delay(end point delay)
= remote-queuing (echoed in the ACK) + Local NIC Rx Delay
(given by t6 − t5)
Fabric delay
= RTT - end point delay
The effective congestion window is combined as min(fcwnd, ecwnd)

## Slide 13: Target Delay
Hop-based scaling :
Fixed base delay + per hop delay
Flow based scaling:
Scale target delay with no of competing flows
Click to ad txt

## Slide 14: Loss Recovery and ACKs
Loss Recovery
  selective acknowledgements(SACK)
  retransmission timeout (RTO)
ACKs - decouple data and ACK packet

## Slide 15: Related Work & Results

## Slide 16: Google Production Takeaways
Comparing results of Swift with GCN / DCTCP.
There are reports for the following:
  Latency / Loss
  Throughput / Utilization

## Slide 17: Near-zero loss rate under high utilization
One of the biggest improvements as we moved traffic to Swift was the reduction in packet loss.
1st graph is loss vs port utilization in Fabric links.
2nd graph is the same axes for ToR hosts.

## Slide 18: Achieves low Latency near the target delay
Graph is between Fabric Link RTT and Cluster throughput.
RTT calculated by NIC timestamps.
Some clusters have RTT above base target due to external factors and flow-based scaling.

## Slide 19: Use of Shared Infrastructure
We share network links with Non-Swift Traffic.
To do so we separate traffic using QoS classes that share link bandwidth using weighted-fair queuing.
this arrangement lets Swift achieve low latency even in cases when a good portion of the traffic is controlled by loss or via GCN.

## Slide 20: Fabric and Host Congestion
Previously tested on mixed shared environments.
This test is on host and fabric separately.
Left is for throughput intensive and Right side is IOPS intensive.
Splitting also helps debugging issue in the respective areas.

## Slide 21: Application Performance
In memory BigQuery Shuffle - Swift’s ability to simultaneously control network delays and host congestion at scale is thus invaluable for this application.
Storage - Swift achieves ∼7% higher IOPS with a 100% success rate in Op-completions, while the losses in GCN resulted in 1.7% of its Ops failing due to deadlines being exceeded.

## Slide 22: Conclusion
There are lots of complex congestion control systems
However, simplicity is proven the best

## Slide 23: Limitations and future scope
Optimal increment functions.
Supporting <10 us latency for short transfer.
Delay can be used for higher-level operations like RPC rate? (RPCs , RMAs)
Is congestion control at packet layer is better than at higher levels?
Can delay be used for fine-grain load balancing and timeouts?

## Slide 24: THANK YOU